Crawford VL3110FCS vertical lifting fabric door

Product description:

Vertical lifting fabric door designed for industrial environments where doors are exposed to moisture, dust, very high or low temperatures or where the door opening is large.

The unique design and structure offers durability, tightness, energy efficiency, operational reliability and minimum maintenance.

Door leaf

Door leaf made out of two layers of very strong vinyl-coated polyester fabric, separated by aluminium intermediate sections.

Intermediate section which gives strength to the door leaf and which creates a buffer between the inside and outside fabric walls.

Wind load is transferred to the vertical guide rails by the horizontal aluminium sections of the door leaf.

The door leaf is available in 8 standard colours.

Door leaf thickness: 100 mm.

Aluminium guide rails.

Bottom section

The bottom section, made of steel and aluminium, is connected to the lifting belt via the safety arresters.

The bottom section contains an optical safety edge and a rubber seal on the bottom edge that creates a seal between the door and the floor.

Optical safety edge.

Safety arresters and wind lock in stainless steel

Safety arresters stop the door if the lifting belt becomes slack or, in an unlikely event, would break.

Wind lock system locks the door when the door is closed.

Surface treatment

Steel components corrosion treatment: category 3 according to ISO 12944.2. Higher class on request. Aluminium, plastic, stainless steel, zinc electroplated steel (~10u). Fixing elements are mainly hot dip galvanized (FZV). Door leaf screws protected with Geomet.

Door features

Door range:

MIN: 1810 mm x (no MIN. height)

MAX (W x H): 6000 x 6000 mm (in combination). Other sizes available on request.

Opening speed: up to 1.5 m/sec.

Temperature range: -35 °C to +70 °C.

Compliance with all operational and safety instructions in EU Directives and the standards of the European Standardisation Committee (CEN).

Wind load (EN 12424)	Class 3-5 (0.7-1.6 kPa, depending on size).

Water resistance (EN 13241)	Class 3, 0.11 kPa (for a closed door).

Air permeability (EN 13241)	Class 2, 12 m3/(m2h).

Thermal transmittance (EN

12428)

Depending on door size, specific data on request.

Sound reduction (ISO 717)	15 dB Rw.

Operating system: Electrical operator.

Dimensions:

x	mm (WxH)

Options: Door leaf

Standard: Polyester, 1100 dtex with plasticised PVC coating

Option: Arctic fabric. For environmental temperatures down to -45°C

Option: Heat resistant fabric with silicone coating

Option: Heat resistant fabric with aluminium coating

Option: Heat resistant fabric with polyurethane coating

Option: Sound reduction fabric

Option: Security fabric

Vision panels

800mm x 800mm

800mm x 1600mm

1300mm x 800mm

1300mm x 1600mm

Fabric color

Tan (RAL 1001)

Red (RAL 3001)

Blue (RAL 5005)

Green (RAL 6009)

Grey (RAL 7004)

Anthracite (RAL 7016)

White (RAL 9016)

Translucent white

Header box

Gear motor on inside of the building

Gear motor on outside of the building

Gear motor in the door opening

Insulated

Stainless steel cladding and motor casing

Self-supporting header box

Operator

Control system PLC-based

Protection class, control cabinet IP65

Protection class, safety boxes IP67

Protection class, motor IP55

Protection class, brake resistor IP51 (with protection)

3/phase 380-480V 50/60Hz power supply

Control voltage 24V DC

Fusing: 20 A / 32 A

Heat and cold resistance, exterior: -35 °C to +70 °C

Heat and cold resistance, inside control unit: -10 °C to +50 °C

Power consumption: 2.2 or 4.1 kW

Options

Radio remote control

“Open" (during closing process) if open button is used - door immediately stops and opens completely)

Pull switch for OPEN / CLOSE

External push-button, key switch

“One-button function” - opens or closes door, depending on actual status (e.g. radio, pull switch)

Additional safety (e.g. photo cell, radar) – door immediately opens completely

Free contacts

Photo cell

Reduced opening height

Radar

Magnetic loop

Warning lights

Emergency power switch

Interlocking door function

Other supplementary equipment

Control cabinet in stainless steel

Heating element in the control cabinet

Emergency power switch

Clamp strip covers in the same colors as the fabric

Side jambs (if posts for installing the guide rails are not available)

Side jambs in stainless steel

Wind deflectors (in combination with jambs)